How to format “{not definied name}” file system:

Default block size: 4 KiB

struct STRUCTURE_INODE {
uint64_t	block[ 5 ];	// direct, indirect, double-indirect, triple-indirect, quadruple-indirect
#define	TYPE_DEFAULT	(1 << 0)
#define	TYPE_DIRECTORY	(1 << 1)
uint64_t	limit;	// file size in Bytes
uint8_t	reserved[ 206 ];	// for future use
uint8_t	type;
uint8_t	name_limit;	// name size in ASCII characters
#define	NAME_LIMIT	255
uint8_t	name[ NAME_LIMIT + 1 ];
} __attribute__( (packed) );	// 512 Bytes

Lets assume we have storage of size 1 MiB, unpartitioned for simplification.

1 MiB = 1048576 Bytes

1048576 / 4096 Bytes = 256 Blocks

By default, empty file system have 1 Superblock and 1 Root Directory. Thanks to that information we can calculate required size of Bitmap

256 Block – 1 Superblock – 1 Root Directory = 254 Blocks left.

254 / (4096 * 8 bits) = 0,007751465 of Blocks, aligned up will give us 1 Block

Preview:

Block ID
0	1	2	3	4	5	...	255
Superblock	Bitmap	Root Directory	{free}	{free}	{free}	...	{free}

Bitmap contains only information about already used blocks, so clean filesystem structure will have footprint like:
			Byte
0	1	2	3	4	5	...­	4095
00000111	00000000	00000000	00000000	00000000	00000000	...	00000000